## Slide 1: Encoders
Abu Humayed Azim Fahmid
Lecturer, CSE Dept., UIU

## Slide 2: Encoders
Does reverse operation to decoder
An encoder has 2n (or fewer) input lines and n output lines
Constraint – only one input is active at a time

## Slide 3: Octal-to-Binary Encoder (8-to-3)

## Slide 4: Octal-to-Binary Encoder (8-to-3)

## Slide 5: Hexadecimal-to-Binary Encoder (16-to-4)

## Slide 6: Hexadecimal-to-Binary Encoder (16-to-4)

## Slide 7: Decimal-to-BCD Encoder (10-to-4)

## Slide 8: Decimal-to-BCD Encoder (10-to-4)

## Slide 9: Priority Encoder
Encoder with priority function
  Multiple inputs may be true simultaneously
  Higher priority input gets the precedence

## Slide 10: 4-Input Priority Encoder

## Slide 11
4-Input Priority Encoder
First let us set the Priority

## Slide 12: 4-Input Priority Encoder
Lowest Priority
First let us set the Priority
Highest Priority

## Slide 13: 4-Input Priority Encoder

## Slide 14: 4-Input Priority Encoder
Here, V is the valid bit
It indicates whether or not there is at least one high-priority input present (i.e., any of the inputs I0, I1, I2 or I3 is 1).

## Slide 15: 4-Input Priority Encoder

## Slide 16: 4-Input Priority Encoder

## Slide 17: 5-Input Priority Encoder
Now, let’s try to ﬁnd equations for a 5-Input Priority Encoder.

## Slide 18: 5-Input Priority Encoder

## Slide 19: 8-Input Priority Encoder
Now, how about 8-Input Priority Encoder with priority: D7>D6>D5>D4>D3>D2>D1>D0
  Can you make the truth table and the equations?
  Try it yourself
  You can avoid the valid bit if you want for this problem

## Slide 20: 8-Input Priority Encoder
Solution:

## Slide 21: Priority Order Can be Different in Problems
For example, let’s try to solve this problem.

## Slide 22: Priority Order Can be Different in Problems
Solution:
D3 D2 D1 D0 |  |  |  | Y1 Y0 |  | V
0 | 0 | 0 | 0 | x | x | 0
 |  |  |  | 0 | 0 | 1
 |  |  |  | 0 | 1 | 1
 |  |  |  | 1 | 0 | 1
 |  |  |  | 1 | 1 | 1

## Slide 23: Priority Order Can be Different in Problems
Solution:
D3 D2 D1 D0 |  |  |  | Y1 Y0 |  | V
0 | 0 | 0 | 0 | x | x | 0
 |  |  |  | 0 | 0 | 1
x x 1 x |  |  |  | 0 | 1 | 1
 |  |  |  | 1 | 0 | 1
 |  |  |  | 1 | 1 | 1

## Slide 24: Priority Order Can be Different in Problems
Solution:
D3 D2 D1 D0 |  |  |  | Y1 Y0 |  | V
0 | 0 | 0 | 0 | x | x | 0
 |  |  |  | 0 | 0 | 1
x x 1 x |  |  |  | 0 | 1 | 1
x 1 0 x |  |  |  | 1 | 0 | 1
 |  |  |  | 1 | 1 | 1

## Slide 25: Priority Order Can be Different in Problems
Solution:
D3 D2 D1 D0 |  |  |  | Y1 Y0 |  | V
0 | 0 | 0 | 0 | x | x | 0
x 0 0 1 |  |  |  | 0 | 0 | 1
x x 1 x |  |  |  | 0 | 1 | 1
x 1 0 x |  |  |  | 1 | 0 | 1
 |  |  |  | 1 | 1 | 1

## Slide 26: Priority Order Can be Different in Problems
Solution:
D3 D2 D1 D0 |  |  | Y1 Y0 |  | V
0 0 | 0 | 0 | x | x | 0
x 0 | 0 | 1 | 0 | 0 | 1
x x | 1 | x | 0 | 1 | 1
x 1 | 0 | x | 1 | 0 | 1
1 0 | 0 | 0 | 1 | 1 | 1

## Slide 27: Priority Order Can be Different in Problems
Solution:
D3 D2 D1 D0 |  |  | Y1 Y0 |  | V
0 0 | 0 | 0 | x | x | 0
x 0 | 0 | 1 | 0 | 0 | 1
x x | 1 | x | 0 | 1 | 1
x 1 | 0 | x | 1 | 0 | 1
1 0 | 0 | 0 | 1 | 1 | 1

## Slide 28: Priority Order Can be Different in Problems
Solution:

## Slide 29
Practice more!!
Check book exercises and previous ﬁnal questions