## Slide 1: Sequential Circuits
Part 3

## Slide 2: The Key Takeaways Obtained So Far
SR Latch
  Truth Table
Trigger
  Level Trigger and Edge Trigger
SR Flip Flop
  Truth Table, Characteristics Table and Excitation Table
D Flip Flop
  Truth Table, Characteristics Table and Excitation Table
JK Flip Flop
  Truth Table, Characteristics Table and Excitation Table
  Racing Problem
  Master Slave JK Flip Flop

## Slide 3: T FLIP FLOP

## Slide 4: T Flip Flop
We can place entire logic circuits inside boxes

## Slide 5: T Flip Flop
We can place all entire logic circuits inside boxes
Only the input and output pins will be shown

## Slide 6: T Flip Flop
We will construct a T flip flop from JK flip flop
T stands for toggle. It will only toggle the content (Q) stored inside

## Slide 7: T Flip Flop
We will construct a T flip flop from JK flip flop
T stands for toggle. It will only toggle the content (Q) stored inside
T
C

## Slide 8: T Flip Flop
What are the possible inputs of J and K now?
T
C

## Slide 9: T Flip Flop
The Three Tables
T
C
C | T | Qn+1
0 | X | Qn
1 | 0 | Qn
1 | 1 | Qn’
Truth Table
Qn | T | Qn+1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Charactersitics Table
Qn | Qn+1 | T
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Excitation Table

## Slide 10: T Flip Flop
The Three Tables
T
C
C | T | Qn+1
0 | X | Qn
1 | 0 | Qn
1 | 1 | Qn’
Truth Table
Qn | T | Qn+1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Charactersitics Table
Qn | Qn+1 | T
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Excitation Table

## Slide 11: FLIP FLOP CONVERSION

## Slide 12: Flip Flop Conversion
The following steps can be followed for flip flop conversion
Identify the available flip flop and the required flip flop
Make the characteristic table for the required flip flop.
Make the excitation table for the available flip flop.
Extend the characteristics table
Write the Boolean expression for the available flip flop
Draw the circuit

## Slide 13: Flip Flop Conversion
Recall Excitation table

## Slide 14: Flip Flop Conversion
Let us perform the following conversions
JK Flip Flop to D Flip Flop
T Flip Flop to D Flip Flop
SR Flip Flop to JK Flip Flop
SR Flip Flop to T Flip Flop

## Slide 15: PRESET AND CLEAR INPUTS

## Slide 16: Preset and clear inputs
Let us consider the following SR Flip Flop for understanding

## Slide 17: Preset and clear inputs
Let us consider the following SR Flip Flop for understanding

## Slide 18: Preset and clear inputs
Let us consider the following SR Flip Flop for understanding
Preset
Clear

## Slide 19: Preset and clear inputs
Let us consider the following SR Flip Flop for understanding
Preset
Clear

## Slide 20: Preset and clear inputs
Let us consider the following SR Flip Flop for understanding
Preset
Clear
Preset | Clear | Qn
0 | 0 | Not Used
0 | 1 | 1
1 | 0 | 0
1 | 1 | Normal Functioning

## Slide 21: Preset and clear inputs
Let us consider the following SR Flip Flop for understanding
Preset
Clear

## Slide 22: STATE DIAGRAMS

## Slide 23: State Diagrams
What is a state?
  In a sequential circuit we will find inputs – A,B,C
  In a sequential circuit we will find outputs – F,E
  In a sequential circuit we will find states
    Q
    Qn
    Qn+1

## Slide 24: State Diagrams
Let us start by making the state diagram of a JK flip flop
Qn | J | K | Qn+1
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Characteristic Table
How the state changes based on input

## Slide 25: State Diagrams
Let us start by making the state diagram of a JK flip flop
Qn | J | K | Qn+1
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Characteristic Table
How the state changes based on input
S0
S1
0x
1x
x0
x1

## Slide 26: Thank You