## Slide 1
Communication Protocols part 1
Arnab Bhattacharjee
Lecturer, Department of CSE,
United International University
Email id : arnab@cse.uiu.ac.bd
Courtesy: Nasif M. Sir,
Md. Shafqat Talukder Rakin Sir

## Slide 2: Serial communication
In Telecommunication and Computer Science, serial communication is the process of sending/receiving data in one bit at a time.

## Slide 3: Parallel communication
Parallel communication is the process of sending/receiving multiple data bits at a time through parallel channels.

## Slide 4: Serial communication

## Slide 5: Parallel communication

## Slide 6: Serial vs Parallel Communication
Serial Communication | Parallel Communication
1. One data bit is transceived at a time | 1. Multiple data bits are transceived at a time
2. Slower | 2. Faster
3. Less number of cables required to transmit data | 3. Higher number of cables required

## Slide 7: Major Factors Limiting Parallel Communication
Speed: Clock skew phenomenon reduces the speed of every link to the slowest of all of the links.
Cable length: Crosstalk phenomenon creates interference between the parallel lines, and the effect only magnifies with the length of the communication link. This limits the length of the communication cable that can be used.
Phenomenon : a fact or situation that is observed to exist or happen, especially one whose cause or explanation is in question.

## Slide 8: Terminology
Clock Skew: In a parallel circuit, clock skew phenomenon is observed, which is the time difference in the arrival of two bits sequentially in adjacent registers. There is a time lag in the data bits through different channels of the same bus. Clock skew is inevitable due to differences in physical conditions of the channels, like temperature, resistance, path length, etc
For example, around 5 people are firing at the same time, there is bound to be a time difference in the arrival of the bullet from the first shooter and that from the second shooter and so on. This time difference is what we call clock skew.

## Slide 9: Terminology
Crosstalk: This phenomenon is observed in parallel circuit when a signal transmitted on one channel of a transmission bus creates an undesired effect in another channel. Undesired capacitive, inductive, or conductive coupling is usually what is called crosstalk, from one circuit, part of a circuit, or channel, to another.

## Slide 10: Advantages of Serial over Parallel
Although a serial link may seem inferior to a parallel one, since it can transmit less data per clock cycle, it is often the case that serial links can be clocked considerably faster than parallel links in order to achieve a higher data rate. A number of factors allow serial to be clocked at a higher rate:
Clock skew between different channels is not an issue
A serial connection requires fewer interconnecting cables (e.g. wires/fibers) and hence occupies less space. The extra space allows for better isolation of the channel from its surroundings.
Crosstalk is not a much significant issue, because there are fewer conductors in proximity.

## Slide 11: UART
UART stands for Universal Asynchronous Receiver Transmitter,
They are basically just a piece of computer hardware that converts parallel data into serial data and vice-versa.
The UART, or Universal Asynchronous Receiver / Transmitter, is a feature of the microcontroller which is useful for communicating serial data (text, numbers, etc.) to the PC. The device changes incoming parallel information (within the microcontroller/PC) to serial data which can be sent on a communication line.

## Slide 12
Super-simplified UART interface. Parallel on one end, serial on the other
Microcontroller

## Slide 13
UART — Data Frame Structure
Each UART byte is wrapped in framing bits that let the receiver detect the start and end of a transmission:
Start
D0
D1
D2
D3
D4
D5
D6
D7
Parity
Stop
Framing overhead (start/stop bits)
Data payload (8 bits = 1 byte)
Parity bit (optional error check)
← Total frame = 10–12 bits to transmit 8 bits of data (overhead ~20–33%)
Baud rate
Common values: 9600, 19200, 38400, 57600, 115200 bps
Data bits
Usually 8 bits (one byte), sometimes 7 or 9
Parity
None, Even, or Odd — for simple error detection
Stop bits
1 or 2 bits — marks end of frame

## Slide 14: USART
USART stands for Universal SynchronousAsynchronous Receiver Transmitter.
In synchronous transmission, the clock data is recovered separately from the data stream and no start/stop bits are used. This improves the efficiency of transmission on suitable channels since more of the bits sent are usable data and not character framing.

## Slide 15
USART — Async vs Sync Frame Comparison
Asynchronous frame (same as UART):
Start
D0
D1
D2
D3
D4
D5
D6
D7
Par
Stop
↑ Start + stop bits add overhead on every byte
Synchronous frame (no start/stop bits — clock does the framing):
CLK:
⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍⎍
Byte 0
Byte 1
Byte 2
Byte 3
Byte 4
Byte 5
…
↑ Continuous stream — every bit carries data. No framing overhead.
Async efficiency
~73–80% — start/stop bits waste 2–3 out of every 10–11 bits
Sync efficiency
~100% — clock line handles framing; all bits carry payload data

## Slide 16
UART vs USART — At a Glance
UART
USART
Mode
Asynchronous only
Async + Synchronous
Clock line
None
Required in sync mode
Start/stop bits
Always required
Not needed in sync mode
Data efficiency
~73–80%
~80% (async) / ~100% (sync)
Speed
Lower (baud rate limited)
Higher in sync mode
Complexity
Simpler hardware & setup
Slightly more complex
Typical use
Debugging, GPS, Bluetooth
SD cards, displays, sensors
Key insight: USART is backward-compatible with UART. A USART peripheral in async mode behaves identically to UART.

## Slide 17: Thank You