## Slide 1: Lecture 3 Inventory
IPE 3401 – Industrial and Operational Management

## Slide 2
A stock or store of goods
What is Inventory?
Independent Demand Items
Demand not related to any other item and primarily influenced by market conditions
Dependent Demand Items
Demand for an item is influenced by the demand of another item
A “typical” firm invests in inventory roughly
30% of its current assets and 90% of its working capital

## Slide 3
Typical Inventory

## Slide 4
Typical Inventory

## Slide 5
Why do we need inventory?
Economies of batch production
Unpredictable or unreliable vendors
Buffer for imbalanced production lines
Buffer for machine downtimes
Safety stock against random demands or uncertain lead-times
Hedge against poor quality
Bi-product from production smoothing
Avoid loss of sales or high cost of backorders
Fill logistics pipeline - resupply time
Display goods to potential customers

## Slide 6
Area | Responsibility | Inventory Goal | Desired Inventory Level
Marketing | Sell the product | Good customer service | High
Production | Make the product | Efficient lot sizes | High
Purchasing | Buy required material | Low unit cost | High
Finance | Provide working capital | Efficient use of capital | Low
Warehousing | Store the product | Efficient use of space | Low
Engineering | Design the product | Avoid obsolescence | low
Conflicting Objectives of Teams

## Slide 7
Raw Material
Material needing further processing
Components that go into the product as is
Supplies such as glue, screws, ink, thread
Dependent demand
Types of Inventory
Work in Process (WIP)
Inventory in the production system waiting to be processed or assembled and may include semi-finished products
Partially complete goods
Dependent demand
Finished Goods
Output of the production process or end items
Demand is usually independent
Finished goods from one manufacturing plant may be raw material for another
Tools and Supplies
Maintenance and Repairs Inventory
In-transit Inventory

## Slide 8
Inventory Management
Establish a system for tracking items in inventory
Make decisions about
When to order
How much to order
Two basic functions

## Slide 9
Inventory
Costs
Inventory Cost
Procurement
Cost
The amount paid to buy the inventory
Holding (carrying) Cost
Cost to carry an item in inventory for a length of time, usually a year
Ordering Cost
Costs of ordering and receiving inventory
Setup Cost
The costs involved in preparing equipment for a job
Analogous to ordering costs
Shortage Cost
Costs resulting when demand exceeds the supply of inventory

## Slide 10
Periodic System
Physical count of items in inventory made at periodic intervals
Vulnerable as inventory state may change drastically between the counting intervals
Inventory Counting Systems
Perpetual Inventory System
System that keeps track of removals from inventory continuously, thus monitoring current levels of each item
An order is placed when inventory drops to a predetermined minimum level
Universal Product Code (UPC) or Bar-code is implemented to track each item
Point-of-sale (POS) system is required

## Slide 11
Inventory Classification System
35 %
15 %
50 %

## Slide 12
Steps of Solving ABC Classification Problem
For each item, multiply inventory volume by unit price to get the inventory value
1
Arrange inventory values in descending order
2
Club top 15% together as A class, next 35% (cumulative 50% including item marginally surpassing 50%) as B class, and bottom 50% as C class
3

## Slide 13
Example of ABC Classification Problem
A manager has obtained a list of unit costs and estimated annual demands for 10 inventory items and now wants to categorize the items on ABC basis. Solve the problem for him.
Item Number | Annual Demand | Unit Cost ($)
1 | 25 | 220
2 | 25 | 330
3 | 24 | 200
4 | 15 | 190
5 | 7 | 750
6 | 10 | 800
7 | 12 | 210
8 | 11 | 900
9 | 80 | 90
10 | 10 | 500

## Slide 14
Solution of
ABC Classification Problem
Step 1
For each item, multiply inventory volume by unit price to get the inventory value
Item Number | Annual Demand | Unit Cost ($) | Annual Inventory Value ($)
1 | 25 | 220 | 5,500
2 | 25 | 330 | 8,250
3 | 24 | 200 | 4,800
4 | 15 | 190 | 2,850
5 | 7 | 750 | 5,250
6 | 10 | 800 | 8,000
7 | 12 | 210 | 2,520
8 | 11 | 900 | 9,900
9 | 80 | 90 | 7,200
10 | 10 | 500 | 5,000

## Slide 15
Solution of
ABC Classification Problem
Step 2
Arrange inventory values in descending order
Item Number | Annual Inventory Value ($) | % | Running % | Class
8 | 9,900 | 17% | 17% | A
2 | 8,250 | 14% | 31% | B
6 | 8,000 | 14% | 45% | B
9 | 7,200 | 12% | 57% | B
1 | 5,500 | 9% | 66% | C
5 | 5,250 | 9% | 75% | C
10 | 5,000 | 8% | 83% | C
3 | 4,800 | 8% | 91% | C
4 | 2,850 | 5% | 96% | C
7 | 2,520 | 4% | 100% | C
Total | 59,270 | 100% |  | 
A
B
C

## Slide 16
Solution of
ABC Classification Problem
Step 3
Club top 15% together as A class, next 35% as B class and bottom 50% as C class
Item Number | Annual Inventory Value ($) | Percentage | Running Percentage | Classification
8 | 9,900 | 17% | 17% | A
2 | 8,250 | 14% | 31% | B
6 | 8,000 | 14% | 45% | B
9 | 7,200 | 12% | 57% | B
1 | 5,500 | 9% | 66% | C
5 | 5,250 | 9% | 75% | C
10 | 5,000 | 8% | 83% | C
3 | 4,800 | 8% | 91% | C
4 | 2,850 | 5% | 96% | C
7 | 2,520 | 4% | 100% | C
An item marginally surpassing cumulative 50% is to be considered as B class

## Slide 17
The Need for
Inventories
Can be Reduced by
Using standardized parts
Improving the forecasting of demand
Using preventive maintenance on equipment and machines
Reducing supplier delivery lead times and increasing delivery reliability
Utilizing reliable suppliers and improving the relationships in the supply chain
Restructuring the supply chain so that the supplier holds the inventory
Developing simpler product designs with fewer parts
Reducing production lead time by using more efficient manufacturing methods

## Slide 18
The Inventory Cycle
Quantity on Hand
Reorder Point
Receive Order
Receive Order
Place Order
Place Order
Receive Order
Usage rate
Lead Time
Order Size, Q
Day
0
5
7
12
14
Order Size, Q
350 Units
Usage rate
50 Units per day
Lead time
2 days
Reorder point
100 units (2 days supply)

## Slide 19
Inventory Cost Curves
Optimal Order Quantity
Order Quantity
Cost
Minimum Total Cost
Ordering Cost Curve
Holding (carrying) Cost Curve
Total Cost
Curve
Holding (Carrying) Cost =
Ordering Cost =
Total Cost =
Q = Order Quantity
H = Holding Cost per Unit per Year
D = Demand per Year
S = Ordering Cost per Order

## Slide 20
Economic Order Quantity (EOQ)
The economic order quantity (EOQ) refers to the ideal order quantity a company should purchase in order to minimize its inventory costs, such as holding costs, shortage costs, and order costs

## Slide 21
Assumptions of EOQ
Only one product is involved
1
Annual demand requirements are known
2
Demand is spread evenly throughout the year i.e., the demand rate is constant
3
Lead time is known and constant
4
Each order is received in a single delivery
5
There are no quantity discounts
6

## Slide 22
Deriving EOQ
Using calculus, we take the derivative of the total cost function and set the derivative (slope) equal to zero and solve for Q
EOQ

## Slide 23
Example 1: EOQ
A local distributor for a national tire company expects to sell approximately 9,600 steel-belted radial tires of a certain size and thread design next year. Annual carrying cost is $16 per tire, and ordering cost is $75. The distributor operates 288 days a year.
a. What is the EOQ?
b. How many times per year does the store reorder?
c. What is the length of an order cycle?
d. What is the total annual cost if the EOQ quantity is ordered?

## Slide 24
Solution of Example 1: EOQ
Given That,
Demand, D = 9600 tires per year
Carrying Cost, H = $16 per unit per year
Ordering Cost, S = $75 per order
a. EOQ, tires
b. Number of orders per year = orders per year
c. Length of order cycle = of a year = days = 9 days
d. Total Cost = (/2) 𝐻 + (𝐷/ ) 𝑆 = (300/2) 16 + (9600/300) 75 = 2400 + 2400 = $4800

## Slide 25
Example 2: EOQ
Piddling Manufacturing assembles security systems. It purchases 3,600 high-definition security cameras a year at $180 each. Ordering costs are $50, and annual carrying costs are 20 percent of the purchase price. Compute the optimal quantity and the total annual cost of ordering and carrying the inventory.
Given That,
Demand, D = 3,600 cameras per year
Carrying Cost, H = $180 x 20% = $36 per unit
Ordering Cost, S = $50 per order
EOQ, security cameras
Total Cost = (/2) 𝐻 + (𝐷/ ) 𝑆 = (100/2) 36 + (3600/100) 50 = 1800 + 1800 = $3600

## Slide 26
EPQ is the batch size that a manufacturer produces periodically to satisfy a certain demand and minimize the production cost.

## Slide 27
Assumptions of EPQ
Only one product is involved
1
Annual demand requirements are known
2
Consumption rate is constant; consumption occurs continuously
3
Production rate is constant; production occurs periodically
4
Lead time is known and constant
5
There are no quantity discounts
6

## Slide 28
Production and Consumption
Production and Consumption
Only Consumption
Only Consumption
2
5
7
10
Day
Quantity
Production Run Size (or EPQ)
Maximum Inventory Level
Cumulative Production
Inventory on Hand
Cycle of Production and Consumption

## Slide 29
Economic Production Quantity Model
Q = No. of pieces per production run
p = Daily production rate
H = Holding cost per unit per year
d = Daily demand/usage rate
t = Length of the production run in days
Quantity
Cost
Holding Cost
Setup Cost
EPQ
Condition of Finding EPQ
Holding Cost = Setup Cost

## Slide 30
Economic Production Quantity Model
Q = No. of pieces per production run
p = Daily production rate
H = Holding cost per unit per year
d = Daily demand/usage rate
D = Annual Demand
t = Length of the production run in days
S = Setup cost per production run
= –
Maximum inventory level
Total produced during the production run
Total used during the production run
= (Maximum inventory level)/2
Average inventory level
Average
inventory level
Annual inventory holding cost
Holding cost per unit per year
= x
= x
No. of pieces per production run, Q
Daily production rate
Total used Length of the production run in days
Annual Production Setup cost

## Slide 31
Economic Production Quantity Model
Q = No. of pieces per production run
p = Daily production rate
H = Holding cost per unit per year
d = Daily demand/usage rate
D = Annual Demand
t = Length of the production run in days
S = Setup cost per production run
From the condition of EPQ,
Holding Cost = Setup Cost
    (Putting in place of Q to denote EPQ)

## Slide 32
Economic Production Quantity Model
Equations
Economic Production Quantity,
Cycle Time
Run Time
Maximum Inventory Level,

## Slide 33
Example 3: EPQ
A toy manufacturer uses 48,000 rubber wheels per year for its popular dump truck series. The firm makes its own wheels, which it can produce at a rate of 800 per day. The toy trucks are assembled uniformly over the entire year. Carrying cost is $1 per wheel a year. Setup cost for a production run of wheels is $45. The firm operates 240 days per year. Determine the –
a. Optimal run size. b. Minimum total annual cost for carrying and setup. c. Cycle time for the optimal run size. d. Run time

## Slide 34
Solution of Example 3: EPQ
Given That,
Demand, D = 48,000 wheels per year
Carrying Cost, H = $1 per wheel per year
Setup Cost, S = $45 per production run
Production Rate, p = 800 wheels per day
Demand rate, d 200 wheels per day
a. Optimal Run Size, EPQ, wheels
b. Minimum Total Cost = Carrying cost + Setup Cost
=

## Slide 35
Solution of Example 3: EPQ
c. Cycle time days
thus a run of wheels will be made every 12 days
d. Run time days
thus each run will require three days to complete

## Slide 36
Reorder Point (ROP)
When the quantity on hand of an item drops to ROP amount,
the item is reordered

## Slide 37
Determinants
of the
Reorder Point
The rate of demand
The lead time
The extent of demand and/or lead time variability
The degree of stockout risk acceptable to management

## Slide 38
Reorder Point Under Certainty
Reorder Point, ROP
d = Demand rate (units per period)
LT = Lead time (same time unit as d)
A – Reorder point
B – Material Received
Time
Lead Time
100 days
Stock
A
B
Reorder
Point
Reorder Stock

## Slide 39
Reorder Point Under Certainty with Safety Stock
A – Reorder point
B – Material Received
Time
Lead Time
100 days
Stock
A
B
Reorder
Point
Reorder Stock
Safety Stock
Reorder Point, ROP
SS = Safety Stock
d = Demand rate (units per period)
LT = Lead time (same time unit as d)

## Slide 40
Example 4: Reorder Point
A famous burger restaurant at Dhaka city has a daily demand of 100 burger buns. However, the burger bun supplier doesn’t provide the bun immediately, rather they take 2 days to deliver.
a. What would be the reorder point of the burger bun? b. If the restaurant decides to keep a safety stock of 80 burger buns, then what would be the reorder point in this case?
a. ROP = d x LT = 100 x 2 = 200 burger buns
b. ROP = SS + (d x LT ) = 80 + (100 x 2) = 280 burger buns

## Slide 41
Quantity Discounts
A quantity discount is an incentive offered to a buyer that results in a decreased cost per unit of goods or materials when purchased in greater numbers.
If quantity discounts are offered, the buyer must weigh the potential benefits of reduced purchase price and fewer orders that will result from buying in large quantities against the increase in carrying costs caused by higher average inventories.
TC=Carrying cost+ Ordering cost+ Purchasing cost=(Q/2)H+(D/Q)S+PD; where P = Unit price

## Slide 42
1st 500 Qty
(0-500)
at $10
2nd 500 Qty
(501-1000)
at $9.3
3rd 500 Qty
(1001-1500)
at $8.5
More than 1500 Qty
(1500+)
at $7
A bicycle manufacturer sells bicycles at $10 in general. However it provides quantity discounts in the following way if the purchased quantity is higher
Impact of Achieving Quantity Discounts
Total Inventory Level
Per Unit Cost
No. of Orders
Quantity Discounts
Total Cost

## Slide 43
EOQ in Quantity Discount Cases
Total Cost, TC =Carrying cost+ Ordering cost+ Purchasing cost (PD)
= (Q/2)H + (D/Q)S + PD, where P = Unit price
Quantity
Cost
EOQ
PD
TC Without PD
TC With PD
0
Adding purchasing cost to the total cost doesn’t change the EOQ
Quantity
Cost
0
45
70
PD @ $2.00 each
TC @ $1.40 each
TC @ $1.70 each
PD @ $1.70 each
PD @ $1.40 each
TC @ $2.00 each
Quantity
Cost
EOQ
0
Decreasing Price
EOQ increases with quantity discounts

## Slide 44
Steps in Analyzing a Quantity Discount
For each discount, calculate Q*
If Q* for a discount doesn’t qualify, choose the smallest possible order size to get the discount
Compute the total cost for each Q* or adjusted value from Step 2
Select the Q* that gives the lowest total cost

## Slide 45
Example 5: Quantity Discount Model
A typical quantity discount schedule of a car manufacturer is given below. The annual demand is 5,000 unit of cars. The holding cost is 20% of the purchasing cost and the ordering cost is $49 per order. Determine the EOQ.
Discount Number | Discount Quantity | Discount (%) | Discount Price (P)
1 | 0 to 999 | no discount | $5.00
2 | 1,000 to 1,999 | 4 | $4.80
3 | 2,000 and over | 5 | $4.75

## Slide 46
1,000
2,000
Total cost $
0
Order quantity
Q* for discount 2 is below the allowable range at point a and must be adjusted upward to 1,000 units at point b
a
b
1st price break
2nd price break
Total cost curve for discount 1
Total cost curve for discount 2
Total cost curve for discount 3
Solution of Example 5: Quantity Discount Model

## Slide 47
Solution of Example 5: Quantity Discount Model
Calculate Q* for every discount using the following formula
700 cars per order
714 cars per order
718 cars per order
1000 cars per order
2000 cars per order

## Slide 48
Solution of Example 5: Quantity Discount Model
Annual Demand, D = 5,000 Ordering Cost, S = $49 per order Holding Cost, H = 20% of Purchasing Cost |  |  |  |  |  | 
Discount Number | Unit Price, P | Order Quantity, Q | Annual Product Cost, P x D | Annual Ordering Cost, (D/Q) x S | Annual Holding Cost, (Q/2) x H | Total
1 | $5.00 | 700 | $25,000 | $350 | $350 | $25,700
2 | $4.80 | 1,000 | $24,000 | $245 | $480 | $24,725
3 | $4.75 | 2,000 | $23.750 | $122.50 | $950 | $24,822.50
∴ EOQ = 1000 units at $4.80